## Slide 1: Visible and Near-IR Telescope onboard HiZ-GUNDAM
Kohji Tsumura, Akihiro Miyasaka (Tokyo City Univ.), Hideo Matsuhara, Akihiro Doi, Keisuke Shinozaki (ISAS, JAXA), Shuji Matsuura (Kwansei Gakuin Univ.), Koji Kawabata (Hiroshima Univ.), Hiroshi Akitaya (Chiba Institute of Technology), Daisuke Yonetoku (Kanazawa Univ.) HiZ-GUNDAM team
The second annual conference of Transformative Research Areas (A), “Multimessenger Astrophysics” 18-20 Nov. 2024

## Slide 2
Time Domain Astronomy & Multi Messenger Astronomy
2
z=1000
z=7
z=12
z=0
z=0.5
z=6
・Gravitational Wave
(Short GRB?)
NS-NS, NS-BH (+ BH-BH)
kilonova
・TeV/PeV neutrino
・SN Shock Breakout
・Tidal Disruption
・Fast Radio Burst
・AGN etc.
・Stellar Flare
・Galactic Transients
・Gamma-Ray Burst (GRB)
First Stars (Pop-III)
Cosmic Reionization
Chemical Evolution
Notes: HiZ-GUNDAM is a space mission for both Time domain ＆ Multi-messenger astronomy, like GW. I would emphasize here that, this mission has very unique capability for GRB in the early Universe with its unique capability, which I will explain in the following

## Slide 3: Problems in early universe exploration with conventional GRB follow-ups
Satellite detection of GRBs; alerting it to the ground
⬇︎within 1 hour
Small (30cm-1m) telescopes will detect the afterglow
⬇Within a few hours~1 day
Identify the redshift with a medium size (2~4m) telescope
⬇︎after about 1 day
Spectroscopic observation of high-redshift GRBs with a large 8-m class telescope
By the time a large telescope observes, the GRB afterglow has faded.
In the 18 years of observations with SWIFT, there have been only two GRBs with z>6.
Moreover, statistical accuracy of these spectra is low…
This situation does not change even after the launch of Einstein Probe and SVOM.
Notes: Current situation of GRB follow-ups is:

## Slide 4: Quick follow-up is a Key to solve this problem
The afterglow is expected to be brighter than 21mag at 1 hour after the burst (in >90% probability)
19
20
21
22
23
24
25
26
Greiner et al. (2009)
400
600
800
1000
2000
Wavelength (nm)
Magnitude
Optical
NIR
Lyα absorption edge
(121.6 nm @ z=8.3)
Photometric Redshift by GROND
1 hour
Gray: Long GRB
Black: Short GRB
Expected Lightcurve for GRBs @ z = 7
Based on Kann et al. (2010)
1 day
Notes: After an initial flash of gamma rays, a longer-lived "afterglow" is usually emitted.
The brightness of this afterglow become darker with time, so quick follow-up observation is important.
However, the ground based telescopes start to observe them after receiving the alert of GRB from satellites.
So there would be a time lag between finding GRB and starting the follow-up observation of GRB afterglow.
In addition, to observe GRB afterglow at high-redshift GRBs, near-infrared observation is important because optical light are absorbed by the neutral hydrogen.

## Slide 5: Our goal with HiZ-GUNDAM
Satellite detection of GRBs; alerting it to the ground
⬇︎within 1 hour
Small (30cm-1m) telescopes will detect the afterglow
⬇Within a few hours~1 day
Identify the redshift with a medium size (2~4m) telescope
⬇︎after about 1 day
Spectroscopic observation of high-redshift GRBs with a large 8-m class telescope
Accelerates the process from GRB discovery to the realization of follow-up observations with large telescopes.
Because redshifts are measured for all GRBs discovered by HiZ-GUNDAM, almost no high redshift GRBs are missed.
Automatic on-board follow-up within 300 sec
Within an half-hour
Make this happen with HiZ-GUNDAM
Competitive M-class HiZ-GUNDAM

## Slide 6: NIRT Wavebands & Redshift
Ch.1
0.5
1.7
2.1
0.9
1.3
Ch.2
Ch.3
Ch.4
z = 6.4
z = 9.7
z = 13.0
Lyman-alpha
 [µm]
z = 16.3
Ch.5
2.5
z = 19.6
HiZ-GUNDAM
NIRT bands
In order to distinguish high-redshift objects from nearby objects reddened by dust, detection of two bands on the long wavelength side is necessary.
Photometric redshifts can be determined with good accuracy up to z < 13.0.
In principle, detection is possible up to z < 19.6
J
H
K
Ground telescope
wavebands

## Slide 7
Wide Field X-ray Monitor
・ Lobster Eye optics
・ pnCCD
Near Infrared Telescope
・ 5-band photometry
HiZ-GUNDAM (High-z Gamma-ray bursts for Unraveling the Dark Ages Mission)
Mission： Time Domain Astronomy
“Multi-messenger astronomy” and “Exploration of the early universe”
Observation strategy
(1) Discovery of GRBs/transients with the wide field X-ray monitor
(2) Automatic repointing (T < 300 sec)
(3) Identification of counterpart with the near infrared telescope
(4) Alert message (T << 1 hour)
(5) Spectroscopic observation with large area telescopes (T 1.5 hr)
Space telescope
8m-class
JWST
Subaru
TMT
GMT
E-ELT
Future 30m-class
We will discover treasured targets from a large amount of transient sources, and provide important observation targets to large area telescopes. We will promote
"exploration of the early universe” & ”MM astronomy"
with all the power of astronomy.
HiZ-GUNDAM (High-z Gamma-ray bursts for Unraveling the Dark Ages Mission)

## Slide 8
Neutral Fraction of H
GRB+
Quasar
Galaxy
(JWST)
Early Epoch Reionization
Late Epoch Reionization
？
Brightest galaxy GN-z11, z=10.60
6 hours exposure (JWST)
Quasar z=7.5 8 hours exposure
Bunker+23
Banados+17
Simulation (Umeda & Harikane)
2 hours exposure (Subaru)
High-redshift GRBs are
- Enough bright - Simple spectrum redshift, xHI, galactic neutral gas, metallicity, ionization bubble size, etc.
GRBs are the best probe for the Cosmic Reionization
Umeda & Harikane

## Slide 9
Further Outcome from HiZ-GUNDAM:
Nucleosynthesis of diverse NS mergers
NS – BH
Infrared = heavy element
IR (red) kilonova (heavy)
Opt (blue) kilonova (light)
Mass
2017
(GW170817、GW＋EM)
NS – NS
We expect “Infrared dominated” kilonova
(Enriched heavy elements, Observed from equatorial direction)
Sensitive Infrared follow-up by HiZ-GUNDAM
2019
(GW190425、GW Only)
2019, 2020
(GW Only)
NS
BH
BH
BH
BH
Mass

## Slide 10: Mission Payload
3
 |  |  | Items | Parameters |  |  |  | 
 |  |  | Telescope type | Offset Optics |  |  |  | 
Items | Parameters |  | Aperture size | 30 cm |  |  |  | 
Energy band (keV) | 0.4 – 4 keV |  | Focal length | 183.5 cm |  |  |  | 
Telescope type: | Lobster Eye Optics |  | F number | F6.1 |  |  |  | 
Module Aperture Size | 192 x 192 mm2 |  | Field of view | 12 arcmin × 12 arcmin |  |  |  | 
Number of Module | 16 |  | FoV per pixel | 2 acsec × 2 arcsec |  |  |  | 
Field of View | 0.5 str (in total) |  | Image size | 3 pixel × 3 pixel |  |  |  | 
Focal length | 300 mm |  | Integration time | 10 minutes (2 minutes x 5 frames) |  |  |  | 
Focal plane detectors | pnCCD array |  | Observation Band (μm) | 0.5−0.9 | 0.9−1.3 | 1.3−1.7 | 1.7−2.1 | 2.1-2.5
Number of pnCCD | 16 |  |  |  |  |  |  | 
Sensitivity | ~1e-10 (erg/cm2/s) for 100 sec |  | Limiting Magnitude mag (AB) | 21.4 | 21.3 | 21.4 | 20.8 | 20.7
Position accuracy | 3 arcmin |  | Focal detector | HyViSi | HgCdTe (H1RG) |  |  | 
Near Infrared Telescope
Focal Plane Image
pnCCD
Lobster Eye Optics
φ300 mm primary
5-band simultaneous photometry
Wide Field X-ray Monitor
Notes: Here I will show the mission instruments, one is Wide Field X-ray monitor, and the another is a near-IR telescope.
The X ray monitor consists of 16 modules of Lobster-Eye Optics and pnCCD focal plane detectors, monitoring 0.5 str simultaneously.
The NIR telescope is a small, 30 cm diameter offset Gregorian telescope, with two focal plane arrays covering 5 photometric bands. Although small diameter telescope, thanks to very low backgropund, the sensitivity is as good as the 2-3 m class telescope in the ground.

## Slide 11: Visible and Near-IR Telescope onboard HiZ-GUNDAM
A reflective (offset Gregorian) telescope with 30 cm aperture
Simultaneous 5-band (visible + 4 NIR) imaging via dichroic mirror and a Kösters prism
Field of View: 15 x 15 arcmin2, two image sensors( visible and NIR)
Telescope shall be below 200 K, while the NIR sensor is below 120 K by only passive, radiative cooling
Telescope structure: all aluminum, athermal design (similarly contraction by cooling)
Currently conceptual design is ongoing for optics, structure and thermal design, and electronics.
可視光検出器
近赤外線検出器

## Slide 12: Project Status and Planed Master Schedule
Down selection review was held in April-May 2023
  The ISAS Executives recommended that the mission scope be "to produce Key Science results through coordinated observations with space and ground-based telescopes that have been alerted from HiZ-GUNDAM”.
Down selection review (re-examination) in March 2024
  Passed for all the review items
  But the selection is on-hold …
New schedule
  Pre-phase-A study continued
  Continued Mid-2026: Down selection Review with two other candidates
  ~2027: Mission Definition Review
  A new target launch : 2034
Mission concept was selected in 2018 as Competitive M-class Mission
Now in the pre-Phase A study in ISAS/JAXA
Notes: We survived the down-selection eview this year , however
due to serious problems in human resources in both ISAS, JAXA and the industries in charge of spacecraft system

## Slide 13: On-going works (FY2024-26)
Double Kösters prism (see K. Tsumura’s presentation)
  A noble beam-splitter splitting incident light into multiple wavelengths
Thermal model analysis of passively cooled telescope (i.e., without mechanical cooler)
  Updating for the new optics
  Two industrial study in parallel
  In house study (see R. Kageyama’s presentation)
Visible-band imaging sensor
BBM development of visible and near-IR telescope

## Slide 14: Imaging sensors
[ Near-IR detector ]
Teledyne H1RG + SIDCAR (or ACADIA) ASIC
Dark current must be <0.3 e-/s from sensitivity requirement
 temperature < 120 K
requirement
[ Visible-band detector ]
Teledyne HyViSI or Canon LI3030SAM
HyViSI is current baseline, but we also seek for the possibility to use commercially available C-MOS detectors
  Cryogenic and radiation tests are on-going
Canon LI3030SAM
TeledyneH1RG
Notes: We are planning to use Teledyne H1RG for HiZ-GUNDAM mission.
To obtaine a good sensitivity, dark current needs to be low, and it depends on the temperature of the detector.
In our currucuration, the detector need to be lower than 150K for channel 2 , and lower than 120 K for channel 3 and 4.
It is difficult to obtain such a low temoerarute only by radation cooling, so a mechanical cooler is required.

## Slide 15: BBM development of Visible and Near-infrared Telescope
Purpose
  Verify the cryogenic optical performance is within the requirement
    demonstration of athermal design (all major structure components are made of Aluminum)
Method
  Modify the existing cryo-vacuum chamber at Kanazawa University
  Image quality at cold is to be measured by introducing a ~30 cmφ collimated beam
Planned Schedule
  FY24: mechanical and thermal design of test configuration
  FY25 1Q-2Q: design and fabrication of BBM mirrors and structures
  FY25 3Q~ : BBM test in the cryo-vacuum chamber at Kanazawa University

## Slide 16
Summary
・ HiZ-GUNDAM will provide us with new scientific opportunity for
(1) exploration of early universe
(2) multi-messenger astronomy
・ A candidate of competitive M-class mission of ISAS/JAXA; the new launch target is around 2034.
Rapid follow-up with the on-board visible and near-IR telescope
  30 cm off-axis telescope, with simultaneous 5-band imaging at 0.5 – 2.5 μm
  Passively cooled (radiatively) telescope (< 200 K), and a near-IR detector (<120 K)
Near future Plan
  Establish the thermal / mechanical design based on industrial study
  FY 2024-25: Design and construction of BBM telescope, verification of athermal design concept
  Mid-2026: down-selection review

## Slide 17: Backup Slides

## Slide 18: 可視光・近赤外線望遠鏡BBM試作・実証（2024－6年度）
課題 | 必要な作業 | 実施担当
BBM鏡の製造に向けた検討 | 鏡の製造に必要な検討を実施 | クリスタル光学
BBM鏡の製造 | 実際の鏡の製造、保持機構(裏面構造)含む | クリスタル光学
鏡単体の評価(常温) | 鏡単体の性能評価(干渉計を用いた測定？) | クリスタル光学
望遠鏡システムとしての評価(常温) | ２枚の鏡を組み合わせた望遠鏡システムとしての性能評価(干渉計を用いた測定？) | クリスタル光学
鏡の保持機構の設計 | オプティカルベンチへの鏡の保持機構(望遠鏡裏面でのねじ止めの方法)の検討(表面形状への影響の解析など) | オプトクラフト
望遠鏡のオプティカルベンチの設計 | 金沢チャンバーに入る支持構造の検討 | オプトクラフト・クリスタル光学
金沢チャンバーでの冷却構造の検討 | 金沢チャンバー内へのBBM望遠鏡の設置および冷却の方法についての検討 | オプトクラフト・TAエンジニアリング
金沢チャンバーの整備 | 30cm光学窓の延長など | 
望遠鏡のオプティカルベンチの製造 | 望遠鏡のオプティカルベンチを製造する | 
低温光学実験で用いるコリメーターの選定 | 低温光学試験で用いる口径>30cmのコリメーターの選定 | 
低温光学実験で用いる検出器の選定 | 低温で駆動する必要あり、解像度は必要だが高感度は不要。購入済みのCanon検出期が候補？ | 
金沢チャンバーを用いた低温光学試験の実施 | BBM望遠鏡を冷却(~160K)して光学試験を実施する | 

## Slide 19
ガンマ線バースト (GRB)
・大質量星の爆発 (M>40Msun)
・E = 1050 – 1054 ergs
・非常に明るいため、遠方宇宙の探査に活用できる
Short GRBs (T < 2 sec): 極限環境物理の探査
・中性子星連星の合体
・E = 1048 – 1051 ergs
・重力波との協調観測
Long GRBs (T > 2 sec): 初期宇宙の探査
中性子星連星
など
Notes: Gamma-ray bursts are extremely energetic exposions and they are the brightest and most energetic electromagnetic events known to occur in the universe
There a re two type of GRBs. One is the long GRBs, which are the Massive star explosions, therefoe we can explorer the eary universe at high-z by observing the long GRBs
The other tyoe of GRBs is the short GRB, which caused by the NS-NS merger eith gravitational wave. Therefore, observing short-GRB is very important for the gravitational wave astronomuy

## Slide 20: GRBを用いた初期宇宙探査の意義
銀河やクェーサーの観測と比較した、GRBでの初期宇宙探査の利点
  銀河と比較してGRB発生直後の残光は数1000倍以上と圧倒的に明るいため、 短時間の観測でもS/N比の高いデータを獲得できる
  大規模な銀河は長期間にわたって輝いているため銀河間空間を電離してしまう（観測バイアスが存在する）が、突発天体であるGRBは爆発より前に銀河間空間へ与える影響はほとんど無いことから、初期宇宙の普遍的な状態を計測できる（無バイアス性の高い計測が可能である）
  銀河やクェーサーのスペクトル形状は複雑で、かつ個性があるためにライマンα吸収端の減衰翼形状の測定が困難であるが、GRBは単純なベキ型のスペクトルであることから同形状を測定しやすい（モデル依存性の少ない計測が可能である）

## Slide 21
Nominal Operation
(1) 120 degrees of solar separation angle and 50 degrees of moving forward
(2) Keeping the inertial pointing during 560 sec HiZ-GUNDAM monitors X-ray transients
(3) The satellite slews to the next nominal pointing
Maneuver
150 sec
Pointing
560 sec
⦿
Solar
Satellite orbit:
Sun-synchronous polar orbit (Twilight)
We observe roughly eight different fields of view in every orbit.
This sequence is optimized for follow-up observations with the NIR telescope, we make sure of more than 10 minutes for 97% GRBs discovered by itself.
KSAT
KSAT
VHF
VHF
Inmarsat
down
uplink

## Slide 23
追観測可能な8m級望遠鏡の分光器の比較
 | Wavelength coverage | Resolution R = R/ΔR | Multiplicity | Notes
Subaru/PFS | Optical + J-band simultaneous | 2000 (blue) 3000 (red) 4000 (NIR) | 2394 fibers | 
Subaru/NINJA | Optical to J, H (+K)-band simultaneous | 5000 | Single object | LTAO => 0.5-1.0 mag deeper than X-shooter
Keck/NIRES | Y, J, H, K simultaneous | 2900 | Single object | 
VLT/X-shooter | Optical to J, H, and K-band simultaneous | 5000 | Single object | 
可視光〜近赤外線を1度の観測でカバーできることが重要
Notes: RIX-17: 黒と灰色のデータ (Watanabe)
RIX-24: 図の意味がわからない (Yamasaki)
RIX-53: 全てのGRBについて描かれているのか (Ouchi)
まず、この図は実際に観測されて距離も測定されたGRBを用いて、もしそれらがz=7に存在したら
どのような光度曲線になるかを示したもので、距離が遠くなる効果、time dilation, 波長依存性 K^correction
を施して変換したもの。
Hiz-GUNDAMの望遠鏡と地上１m望遠鏡で検出できる割合を比較すると、
感度を換算しただけの場合は6〜7倍多く、
地上１ｍに近赤外線望遠鏡が付いていることは稀であることから、
それを含めると20〜40倍程度と考えられる。