## Slide 1: First Light with the Protoype Schwarzschild-Couder Telescope’s Upgraded Camera
Zachary Curtis-Ginsberg, UW-Madison On behalf of the CTAO-SCT Collaboration and the CTAO Consortium
TeVPA 2026, Tendo, Japan
September 2nd, 2026

## Slide 2: Imaging Atmospheric Cherenkov Telescopes
Zach Curtis-Ginsberg, pSCT First Light, 9/2/26
Imaging atmospheric Cherenkov telescopes (IACTs) detect Cherenkov light from extensive air showers
Those images are used to reconstruct the incident gamma rays (and cosmic rays)

## Slide 3: CTAO
Zach Curtis-Ginsberg, pSCT First Light, 9/2/26
Cherenkov Telescope Array Observatory
  Next generation gamma-ray observatory
Full sky coverage
  Two IACT arrays: La Palma, Spain & Paranal, Chile
20 GeV to 300 TeV energy range
  Large-Sized Telescope (LST): 20 GeV to 3 TeV
  Medium-Sized Telescope (MST): 80 GeV to 50 TeV
  Small-Sized Telescope (SST): 2 TeV to 300 TeV
Both arrays under construction

## Slide 4: SCT
Schwarzschild-Couder Telescope (SCT)
Medium-sized dual mirror telescope
Dual-mirror design improves point spread function across the entire field of view, enabling better angular resolution
Zach Curtis-Ginsberg, pSCT First Light, 9/2/26

## Slide 5: Prototype SCT (pSCT)
Located at the Fred Lawrence Whipple Observatory in Arizona, USA
  Co-located with VERITAS
Dual-mirror optical system
  Good optical resolution across the entire field of view
  Fine pixel resolution to match the optical resolution
8° field of view with almost constant point spread function (PSF)
Zach Curtis-Ginsberg, pSCT First Light, 9/2/26
Notes: Small plate scale: 1.625 mm per arcminute with an 80 cm focal plane
PSF 0.05-0.07°

## Slide 6: pSCT Camera
Modular camera with 9 sectors
177x 64-pixel camera modules
11,328x 6x6 mm silicon photomultiplier pixels
  0.067° per side
Original camera detected the Crab Nebula in 2020 with only the central sector
Zach Curtis-Ginsberg, pSCT First Light, 9/2/26

## Slide 7: pSCT Camera Upgrade
Ongoing upgrade to improve camera electronics and mechanics
Will fully populate the camera
Updated electronics with reduced crosstalk and trigger noise
JATIS Volume 12 Issue 3 Article 034001 (2026)
Zach Curtis-Ginsberg, pSCT First Light, 9/2/26
Notes: Cherenkov TARGET C
Chrenkov TARGET 5 Trigger Extension ASIC
SiPM multichannel ASIC for high Resolution Cherenkov Telescopes
TeV Array Readout Electronics with GSa/s sampling and Event Trigger

## Slide 8: Mono-pSCT Simulations
Zach Curtis-Ginsberg, pSCT First Light, 9/2/26
Point source sensitivity of the mono-pSCT full camera
Comparable in its core energy range with other mono telescopes
Very little loss in sensitivity for off-axis observations

## Slide 9: Mono-pSCT Simulations
Zach Curtis-Ginsberg, pSCT First Light, 9/2/26
Observation duration to detect a point source across a broad range of fluxes
10% Crab source takes ~5 hours of observations for a 5σ detection
~1 order of magnitude less sensitive than VERITAS
  Under Crab spectrum assumptions

## Slide 10: First Sector Installation
22 modules installed April 1st 2026
Zach Curtis-Ginsberg, pSCT First Light, 9/2/26

## Slide 11: First Light April 2nd ‘26
Zach Curtis-Ginsberg, pSCT First Light, 9/2/26
First light was achieved with…
  Camera out of focus
  Mirrors dirty
  98% moonlight
    Demonstrates the increased robustness and observing time of SiPM cameras
  No module calibrations applied

## Slide 12: PSF Optimization
Camera has 3D motion control
Pointing at the bright star Arcturus and moving the camera to/from the focal point to optimize the point spread function
Further optimization of the optical alignment is planned
Zach Curtis-Ginsberg, pSCT First Light, 9/2/26
Notes: Current PSF measured to be ~3.7’

## Slide 13: Star Tracking
Using waveform baseline variance from night sky background events
Stacking thousands of events to increase signal-to-noise
Saturated peaks come from colorbar limit
Zach Curtis-Ginsberg, pSCT First Light, 9/2/26

## Slide 14: Commissioning Example
Cherenkov ring from a muon followed ~8ns later by a cosmic-ray shower
Demonstrates the concept of imaging atmospheric Cherenkov telescopes -> muon reaches the ground before the Cherenkov light
Zach Curtis-Ginsberg, pSCT First Light, 9/2/26

## Slide 15: Markarian 421 Observations
Example run
Shower candidate rate is constant at ~80 Hz
  Events surviving basic cleaning and filtering
  True shower rate is lower
Night sky background changes increase all event rate
Preliminary
Zach Curtis-Ginsberg, pSCT First Light, 9/2/26

## Slide 16: Markarian 421 Observations
0
5
10
15
20
25
Zach Curtis-Ginsberg, pSCT First Light, 9/2/26
p.e.
The pSCT is ~35 meters from VERITAS T4
Matched cosmic ray
Central circles are 0.5° radius
Notes: Likely a few TeV
~10 m impact position for pSCT

## Slide 17: Markarian 421 Observations
Matched bright cosmic ray
0
175
200
150
Zach Curtis-Ginsberg, pSCT First Light, 9/2/26
125
100
p.e.
75
50
25
Central circles are 0.5° radius
Notes: Medium impact (~50-100 m)

## Slide 18: Markarian 421 Observations
Matched 3.4 TeV gamma ray
Zach Curtis-Ginsberg, pSCT First Light, 9/2/26
0
20
40
60
80
100
p.e.
Central circles are 0.5° radius
Notes: Impact ~125-150 m from pSCT (162 m from T4)

## Slide 19: Markarian 421 Observations
Matched 3.4 TeV gamma ray (162 m from T4)
Zach Curtis-Ginsberg, pSCT First Light, 9/2/26
0
20
40
60
80
100
p.e.
pSCT
Offline matching of cosmic rays and gamma rays is robust
  ~15 Hz rate of matched showers
An important step towards possible integration of the pSCT as part of an IACT array
Notes: Impact ~125-150 m from pSCT (162 m from T4)

## Slide 20: Next Steps
52 more camera modules are in Wisconsin for optimization, calibration, assembly, and testing
They will be installed this fall
The final 103 modules will follow after that
Simulations of the mono-pSCT are in development, with further work to improve SCT array simulations
Zach Curtis-Ginsberg, pSCT First Light, 9/2/26

## Slide 21: Summary
The pSCT camera upgrade is underway
Installation and first light of 22 camera modules
Gamma-ray coincidence matching with VERITAS during initial Markarian 421 observations
52 more modules are expected to be installed this fall
The last 103 modules are expected to be installed in 2027
Zach Curtis-Ginsberg, pSCT First Light, 9/2/26

## Slide 22: Thank you! curtisginsbe@wisc.eud
Zach Curtis-Ginsberg, pSCT First Light, 9/2/26

## Slide 23: Backup
Zach Curtis-Ginsberg, pSCT First Light, 9/2/26

## Slide 24: CTAO Alpha Configuration
Northern Array: 20 GeV - 5 TeV, 4 LST, 9 MST
Southern Array: 150 GeV - 300 TeV, 14 MST, 37 SST
Source: CTAO
Zach Curtis-Ginsberg, pSCT First Light, 9/2/26
Notes: There has been funding for 2 LSTs and 5? more SSTs in the south now

## Slide 25: CTAO Sensitivity
Source: CTAO
Minimum flux needed for 5σ detection of a point source with 50 hours of exposure (or instrument equivalent)
  For the alpha configuration
Comparing CTAO to other current and upcoming instruments
Zach Curtis-Ginsberg, pSCT First Light, 9/2/26

## Slide 26: CTAO-US
17 US institutions, 50+ current members
Development of the pSCT/SCT instrument
CTAO leadership contributions
  Co-spokesperson
  Science Coordinator
  Science working group leads
  SAPO leadership/members
  Science and technology development
  White papers leadership
Zach Curtis-Ginsberg, pSCT First Light, 9/2/26

## Slide 27: SC Vs. DC Medium Sized Telescope
Source: D. Nieto et al. “Construction of a medium-sized Schwarzschild-Couder telescope as a candidate for the Cherenkov Telescope Array: development of the optical alignment system”, J-F. Glicenstein. “Status of the Davies-Cotton and Schwarzschild-Couder Medium-Sized Telescopes for the Cherenkov Telescope Array”
Zach Curtis-Ginsberg, pSCT First Light, 9/2/26

## Slide 28: SC Optics
Focal length 5.586m
Aperture 9.66m
Source: J. Rousselle et al. “Construction of a Schwarzschild-Couder telescope as a candidate for the Cherenkov Telescope Array: status of the optical system”
Zach Curtis-Ginsberg, pSCT First Light, 9/2/26
Notes: Schwarzschild-Couder design is isochronous, no spherical or comatic aberrations
2nd mirror is defocusing, located ~halfway along the focal length of 1st mirror
This defocusing gives the higher image resolution and smaller focal plate scale
Focal plan is curved

## Slide 29: SC Optics
9.7m primary, 5.4m secondary
48 segments on primary, 24 segments on secondary
On-axis PSF ~3.2’
Measurement
Simulation
Zach Curtis-Ginsberg, pSCT First Light, 9/2/26

## Slide 30: pSCT & VERITAS Locations
Zach Curtis-Ginsberg, pSCT First Light, 9/2/26

## Slide 31: pSCT Crab Detection
Observation campaign of the Crab Nebula in 2020
17.6 hours of data
8.6σ detection
Source: C. Adams et al. “Detection of the Crab Nebula with the 9.7 m Prototype Schwarzschild-Couder Telescope”
Zach Curtis-Ginsberg, pSCT First Light, 9/2/26
Notes: VERITAS generally sees ~1 Hz of gammas from the Crab and ~400 Hz of cosmic rays (cuts preserve ~85% of gammas and ~1% of hadrons)
pSCT with this data saw ~0.005 Hz of gammas from the Crab and ~1.5 Hz hadrons (pre-cuts)

## Slide 32: pSCT Crab Detection
Source: C. Adams et al. “Detection of the Crab Nebula with the 9.7 m Prototype Schwarzschild-Couder Telescope”
Zach Curtis-Ginsberg, pSCT First Light, 9/2/26
Notes: Cuts were helped by looking at the Crab with VERITAS and using its gammaness as truth
Distance is length of ray angle alpha below perpendicular
Black is events off source, red is events on source
Alpha is angle from Crab

## Slide 33: Star Tracking
Red X are peaks in the stacked variance image
Yellow + are stars expected in the field
Using solved star field to calculate source position (Markarian 421)
Zach Curtis-Ginsberg, pSCT First Light, 9/2/26

## Slide 34: Markarian 421 Observations
Matched cosmic ray
0
5
10
15
20
25
Zach Curtis-Ginsberg, pSCT First Light, 9/2/26
p.e.
pSCT
Notes: Likely a few TeV
~10 m impact position for pSCT

## Slide 35: Markarian 421 Observations
Matched bright cosmic ray
0
175
200
150
Zach Curtis-Ginsberg, pSCT First Light, 9/2/26
125
100
p.e.
75
50
25
pSCT
Notes: Medium impact (~50-100 m)

## Slide 36: Markarian 421 Observations
Matched 1.5 TeV gamma ray
Zach Curtis-Ginsberg, pSCT First Light, 9/2/26
0
5
10
15
25
30
p.e.
20
Central circles are 0.5° radius
Notes: Impact ~200-250 m from pSCT (221 m from T4)

## Slide 37: Markarian 421 Observations
Matched 1.5 TeV gamma ray (221 m from T4)
Zach Curtis-Ginsberg, pSCT First Light, 9/2/26
0
5
10
15
25
30
p.e.
20
pSCT
Notes: Impact ~200-250 m from pSCT (221 m from T4)

## Slide 38: Markarian 421 Observations
Matched 1 TeV gamma ray (falls almost on top of pSCT)
Zach Curtis-Ginsberg, pSCT First Light, 9/2/26
0
5
10
15
20
25
30
p.e.
Central circles are 0.5° radius
Notes: Low impact (< 20 m)

## Slide 39: Markarian 421 Observations
Matched 1 TeV gamma ray (falls almost on top of pSCT)
Zach Curtis-Ginsberg, pSCT First Light, 9/2/26
0
5
10
15
20
25
30
p.e.
pSCT
Notes: Low impact (< 20 m)

## Slide 40: Markarian 421 Observations
Spatial location of Hillas centroid for all shower candidates
29 minute run
Preliminary
Zach Curtis-Ginsberg, pSCT First Light, 9/2/26

## Slide 41: SCT Array
Adding 11 SCTs improves performance more than 11 DC-MSTs
The off-axis improvement is even larger
Updated simulations are in development
Zach Curtis-Ginsberg, pSCT First Light, 9/2/26
1
1