## Slide 1
Tailin Zhu
on behalf of the TRIDENT Collaboration
Tsung-Dao Lee Institute, Shanghai Jiao Tong University
TeVPA 2026
2026/09/01
Development of a real-time in-situ calibration system for deep-sea neutrino telescopes
(t.zhu@sjtu.edu.cn)

## Slide 2
Event reconstruction uses the timing, charge and spatial distribution of detected photons.
Some calibration inputs enter detector-response model used in event reconstruction.
Medium: scattering and absorption; Optical background
Geometry: DOM position and orientation; String motion
Sensor response: PMT/SiPM efficiency, timing, waveform
Calibration Input
1
Tailin Zhu (TDLI) | In-situ Calibration System for Deep-sea Neutrino Telescope | TeVPA 2026 | 
Reconstruction
Hypothesis
Likelihood calculation
Physics output
Direction
Energy
Flavour
Calibration Purposes
In the deep sea, these conditions evolve with time → calibration must be in situ and time-dependent.
Photon hit time / number
Photon spatial distribution
Photon waveform
Detector Response
TRIDENT Simulation
Track
Cascade

## Slide 3
Event reconstruction uses the timing, charge and spatial distribution of detected photons.
Some calibration inputs enter detector-response model used in event reconstruction.
Medium: scattering and absorption; Optical background
Geometry: DOM position and orientation; String motion
Sensor response: PMT/SiPM efficiency, timing, waveform
Calibration Input
1
Tailin Zhu (TDLI) | In-situ Calibration System for Deep-sea Neutrino Telescope | TeVPA 2026 | 
Reconstruction
Hypothesis
Likelihood calculation
Physics output
Direction
Energy
Flavour
Calibration Purposes
In the deep sea, these conditions evolve with time → calibration must be in situ and time-dependent.
Photon hit time / number
Photon spatial distribution
Photon waveform
Detector Response
TRIDENT Simulation
Track
Cascade

## Slide 4
Photon hit time / number
Photon spatial distribution
Photon waveform
Medium: scattering and absorption; Optical background
Geometry: DOM position and orientation; String motion
Sensor response: PMT/SiPM efficiency, timing, waveform
Calibration Input
1
Tailin Zhu (TDLI) | In-situ Calibration System for Deep-sea Neutrino Telescope | TeVPA 2026 | 
Detector Response
TRIDENT Simulation
Reconstruction
Hypothesis
Likelihood calculation
Physics output
Direction
Energy
Flavour
Calibration Purposes
Track
Cascade
In the deep sea, these conditions evolve with time → calibration must be in situ and time-dependent.
Event reconstruction uses the timing, charge and spatial distribution of detected photons.
Some calibration inputs enter detector-response model used in event reconstruction.

## Slide 5
The Need for Real-Time Deep-Sea Calibration
TRIDENT Preliminary
1
Tailin Zhu (TDLI) | In-situ Calibration System for Deep-sea Neutrino Telescope | TeVPA 2026 | 
Detector Geometry
Sea currents may move the strings
DOM positions measured with acoustic sensors
TRIDENT site, stable current speeds typically below 10cm/s over 1-year

## Slide 6
1
Tailin Zhu (TDLI) | In-situ Calibration System for Deep-sea Neutrino Telescope | TeVPA 2026 | 
Optical Background
40K and bioluminescence affect the observed hit rate and constitute a background
Water Optical Properties
Absorption and scattering affect photon survival and arrival times
Y. Wang, et. al., PoS (ICRC 2025) 1209
F. Zhang (TAUP 2025)
The Need for Real-Time Deep-Sea Calibration
TRIDENT Preliminary

## Slide 7
~ 60 m
1
TRIDENT Phase-1
Tailin Zhu (TDLI) | In-situ Calibration System for Deep-sea Neutrino Telescope | TeVPA 2026 | 
hDOM
Acoustic emitter/receiver
Junction boxes
Electro-optical cable
Float
Calib. optical receivers
Light system
Isotropic light
Hydrographic sensor
10 optical strings;
200 hybrid-DOMs
Real-time data transmitting and power supply
Sub-ns time sync between calibration string and hDOMs
Y. Wang, et. al., PoS (ICRC 2025) 1209
J. Wu, et. al., JINST 20 P07035 (2025)
A dedicated calibration string
W. Tian, et. al., NIM-A, 1076 170489 (2025)
W. Li, et. al., NIM-A, 1056 168588 (2023)
SiPMs:
< 0.3 ns jitter
PMTs:
< 2ns TTS
~30% QE
42 cm
Z. Wei, et. al., PoS (ICRC 2023) 1213
700 m
70-110 m
Fibre
375 V Power

## Slide 8
1
TRIDENT Phase-1
Tailin Zhu (TDLI) | In-situ Calibration System for Deep-sea Neutrino Telescope | TeVPA 2026 | 
700 m
70-110 m
10 optical strings;
200 hybrid-DOMs
SiPMs:
< 0.3 ns jitter
PMTs:
< 2ns TTS
~30% QE
~ 60 m
42 cm
Fibre
375 V Power
Real-time data transmitting and power supply
Sub-ns time sync between calibration string and hDOMs
Y. Wang, et. al., PoS (ICRC 2025) 1209
J. Wu, et. al., JINST 20 P07035 (2025)
Z. Wei, et. al., PoS (ICRC 2023) 1213
A dedicated calibration string
W. Tian, et. al., NIM-A, 1076 170489 (2025)
W. Li, et. al., NIM-A, 1056 168588 (2023)
hDOM
Acoustic emitter/receiver
Junction boxes
Electro-optical cable
Float
Calib. optical receivers
Light system
Isotropic light
Hydrographic sensor

## Slide 9
Water Optical Calibration
Light Receiving Module: Camera + PMT
Light Emitting Module: Continuous + pulsed modes
Two receiver distances → attenuation from relative intensity
Camera image halo → sensitivity to scattering
PMT SPE arrival-time distributions → absorption + scattering
Validated at previous site expeditions in 2021 and 2024
1
Tailin Zhu (TDLI) | In-situ Calibration System for Deep-sea Neutrino Telescope | TeVPA 2026 | 
GigE Camera: 5M pixels, 12 bit
25 mm lens: 16° viewing angle
Y. Wang, et. al., PoS (ICRC 2025) 1209
W. Tian, et. al., NIM-A, 1076 170489 (2025)
Goal: monitor water optical properties on timescales of seconds at multiple wavelengths.

## Slide 10
Water Optical Calibration
Light Receiving Module: Camera + PMT
Light Emitting Module: Continuous + pulsed modes
Two receiver distances → attenuation from relative intensity
Camera image halo → sensitivity to scattering
PMT SPE arrival-time distributions → absorption + scattering
Validated at previous site expeditions in 2021 and 2024
1
Tailin Zhu (TDLI) | In-situ Calibration System for Deep-sea Neutrino Telescope | TeVPA 2026 | 
GigE Camera: 5M pixels, 12 bit
25 mm lens: 16° viewing angle
Y. Wang, et. al., PoS (ICRC 2025) 1209
W. Tian, et. al., NIM-A, 1076 170489 (2025)
Goal: monitor water optical properties on timescales of seconds at multiple wavelengths.

## Slide 11
Pulsed LEDs with < 5 ns pulse width; 1-10kHz;
Same pulsed light source for PMT response and inter-DOM timing offsets.
Continuous emitting mode supports camera-based water monitoring
396 nm
420 nm
455 nm
480 nm
525 nm
One light system, two calibration functions:
water optics + timing response
1
Tailin Zhu (TDLI) | In-situ Calibration System for Deep-sea Neutrino Telescope | TeVPA 2026 | 
The Light System
The light source non-uniformity

## Slide 12
Geometry: Acoustic Positioning
Piezo-acoustic sensors:
sensitive to 10k-70k Hz, -160 dB
Acoustic receivers integrated in hDOMs
Transmitters are deployed at string junction boxes
1
Tailin Zhu (TDLI) | In-situ Calibration System for Deep-sea Neutrino Telescope | TeVPA 2026 | 
J. Liu, et. al., Ocean Engineering, 347 124038 (2026)
< 20 cm hDOM positioning precision is targeted to support sub-ns photon timing and ~0.1° track angular resolution at ~100 TeV.

## Slide 13
Geometry: Acoustic Positioning
Piezo-acoustic sensors:
sensitive to 10k-70k Hz, -160 dB
Acoustic receivers integrated in hDOMs
Transmitters are deployed at string junction boxes
1
Tailin Zhu (TDLI) | In-situ Calibration System for Deep-sea Neutrino Telescope | TeVPA 2026 | 
J. Liu, et. al., Ocean Engineering, 347 124038 (2026)
< 20 cm hDOM positioning precision is targeted to support sub-ns photon timing and ~0.1° track angular resolution at ~100 TeV.

## Slide 14
Geometry: Acoustic Positioning
1
Tailin Zhu (TDLI) | In-situ Calibration System for Deep-sea Neutrino Telescope | TeVPA 2026 | 
J. Liu, et. al., Ocean Engineering, 347 124038 (2026)
Hydrographic measurements provide environmental inputs to the acoustic positioning model.
  Sound velocity + sea current profile
Real-time environmental inputs for acoustic positioning

## Slide 15
Optical Background: Bioluminescence
Correlation between bioluminescence and sea currents observed.
Hydrographic data → environmental inputs for background modelling
1
Tailin Zhu (TDLI) | In-situ Calibration System for Deep-sea Neutrino Telescope | TeVPA 2026 | 
F. Zhang (TAUP 2025)
F. Zhang (TAUP 2025)
TRIDENT Preliminary
TRIDENT Preliminary
103 -105 trigger-rate bursts observed on seconds timescales
Camera + PMT: intensity, spatial and spectral information
Aim: monitor background rate, variability, and environmental correlations

## Slide 16
Optical Background: Bioluminescence
Correlation between bioluminescence and sea currents observed.
Hydrographic data → environmental inputs for background modelling
1
Tailin Zhu (TDLI) | In-situ Calibration System for Deep-sea Neutrino Telescope | TeVPA 2026 | 
F. Zhang (TAUP 2025)
F. Zhang (TAUP 2025)
TRIDENT Preliminary
TRIDENT Preliminary
103 -105 trigger-rate bursts observed on seconds timescales
Camera + PMT: intensity, spatial and spectral information
Aim: monitor background rate, variability, and environmental correlations

## Slide 17
Independent Muon Tagging
MuonSLab has demonstrated stable muon counting in deep-sea measurements.
For TRIDENT, a scintillator-based tag provides an independent particle reference for detector studies and muon-calibration development.
4 x 20 cm x 20 cm x 2 cm slabs
SiPM readout: millimeter-level spatial resolution
Plastic sinctillator + SiPM
1
Tailin Zhu (TDLI) | In-situ Calibration System for Deep-sea Neutrino Telescope | TeVPA 2026 | 
J. Wu, et. al., JINST 20 P07035 (2025)

## Slide 18
Status
1
Tailin Zhu (TDLI) | In-situ Calibration System for Deep-sea Neutrino Telescope | TeVPA 2026 | 
See Fuyudi Zhang’s talk on 2026/09/01
The First Long-Term In-situ Performance of a Prototype Demonstrator for TRIDENT Neutrino Telescope
Validated in sea trials
Optical calibration strategy
Muon tagging
Deepsea conditions characterised
Bioluminescence and environmental correlations

## Slide 19
Conclusion
1
Tailin Zhu (TDLI) | In-situ Calibration System for Deep-sea Neutrino Telescope | TeVPA 2026 | 
A compact multi-purpose calibration system is under development
Attenuation-length measurements using cameras and PMTs in 2021 and 2024 sea trials show consistency
Optical background: camera + PMT + hydrographic information characterise background intensity and variability.
Timing: pulsed LED + White Rabbit provide precise inter-DOM timing calibration.
Geometry: precise acoustic positioning required underwater.
Independent muon tagging: dedicated scintillator-based modules prepared.
Target Phase-1 operation: 2027

## Slide 20
Running in the Dark, Calibrating the Way ...
1
Tailin Zhu (TDLI) | In-situ Calibration System for Deep-sea Neutrino Telescope | TeVPA 2026 | 
(Pic credit: Yingwei Wang)
Thank you!

## Slide 21
Backup
1
Tailin Zhu | In-situ Calibration System for Deep-sea Neutrino Telescope | TeVPA 2026 | 

## Slide 22
TRIDENT
Detector design:
Penrose tiling – Irregular 70-110 m string spacing.
Curved wider pathways for inner string access, to reduce muon corridor events
Hong Kong
Sanya
480 km
Planned for 8km3 in South China Sea
3.5 km deep, flat plane site chosen
Close to equator for full-sky coverage
Scientific goals:
Point source searches
All-flavour detection @ 100 GeV – EeV
1
Tailin Zhu | In-situ Calibration System for Deep-sea Neutrino Telescope | TeVPA 2026 | 

## Slide 23
Acoustic Positioning system
In total 11 transmitters, at least 5 will be used for positioning
1
Tailin Zhu | In-situ Calibration System for Deep-sea Neutrino Telescope | TeVPA 2026 | 
J. Liu, et. al., Ocean Engineering, 347 124038 (2026)