## Slide 1
2026/08/30 – 09/04 TeVPA @ Tendo, Yamagata, Japan
HiZ-GUNDAM pre-project candidate team
Daisuke YONETOKU (Kanazawa University)
・ Competitive M-class mission (Epsilon mission) in JAXA
・ Launch target is ~FY2034 …

## Slide 2
HiZ-GUNDAM： Promotion of Time Domain Astronomy
Key Science 1: Multi-Messenger Astronomy
Identification/localization of E-M counterparts associated with GW and neutrino
Transition from gravitational energy to heavy element (kilonova) and particles
Diversities of multi messenger sources from X-ray to optical/NIR observation
Key Science 2: Exploration of early universe with GRB
(1) GRB rate at z > 6
(2) Reionization history
(3) First heavy metals
(4) Survey of Pop-III GRBs
Planck HP
z=1000
z=7
z=12
z=0
z=0.5
z=6
These observations require both “wide field monitor” and “near-infrared follow-up”

## Slide 3
HiZ-GUNDAM (High-z Gamma-ray bursts for Unraveling the Dark Ages Mission)
Mission： Time Domain Astronomy
“Multi-messenger astronomy” and “Exploration of the early universe”
We will discover treasured targets from a large amount of transient sources, and provide important observation targets to large area telescopes.
We will promote "early space exploration” and ”MM astronomy"
with all the power of astronomy.
Space telescope
8m-class
JWST
Subaru
TMT
GMT
E-ELT
Future 30m-class
TAO
・ Lobster Eye Optics
・ pnCCD imaging detector
・ Simultaneous 5-band photometry
・ 0.5 – 2.5 um
MONSTER: Multiband Optical and Near-infrared Simultaneous Telescope for Efficient Response
EAGLE: Exploration of Ancient GRBs with Lobster Eye
Observation strategy
(1) Discovery of GRBs/transients with the wide field X-ray monitor (t < 0 sec)
(2) Automatic repointing (t < 300 sec)
(3) Identification of counterpart with the near infrared telescope (t ~ 1000 sec)
(4) Alert message (t ~ 0 sec for X-ray, ~ 1800 sec for Opt/NIR)
(5) Spectroscopic observation with large area telescopes (t ~ 1.5 hour)

## Slide 4
EAGLE (Wide Field X-ray Monitor)
Items | Parameters
Energy band (keV) | 0.4 – 4 keV
Telescope type: | Lobster Eye Optics
Number of Modules | 16
Field of View | 0.53 str (16 modules)
Focal length | 300 mm
Focal plane detectors | pnCCD array
Time resolution | < 100 msec
Sensitivity | ~ 1e-10 (erg/cm2/s) For 100 sec
Position accuracy | 3 arcmin
20μm
5μm
Micro Pore (Lobster Eye) Optics
Focal Image
pnCCD (Focal Imaging Detector)
55 mm
Requirements for the focal plane detector | 
Sensitive Area | > 55 × 55 mm2
Pixel Size | 108 μm
Depletion Layer | 450 μm
Quantum efficiency | > 90% @ 0.4 – 4 keV
Frame rate | ≥ 10 fps

## Slide 5
Items | Parameters |  |  |  | 
Telescope type | Offset Optics |  |  |  | 
Aperture size | 30 cm |  |  |  | 
Focal length | 183.5 cm |  |  |  | 
F number | F6.1 |  |  |  | 
Field of view | 15 arcmin × 15 arcmin |  |  |  | 
FoV per pixel | 2 acsec × 2 arcsec |  |  |  | 
Image size | 3 pixel × 3 pixel |  |  |  | 
Integration time | 10 minutes (2 minutes x 5 frames) |  |  |  | 
Observation Band (μm) | 0.5−0.9 | 0.9−1.3 | 1.3−1.7 | 1.7−2.1 | 2.1-2.5
Limiting Magnitude mag (AB) 10min, 10σ | 21.3 | 20.9 | 20.6 | 20.5 | 20.4
Focal detector | HyViSi | HgCdTe (H1RG) |  |  | 
5-band simultaneous photometry
Telescope
T < 200 K
NIR imaging
Detector T < 120 K
Primary Mirror
φ300 mm
MONSTER (Near Infrared Telescope)
Kohji TSUMURA’s Talk
Thermal Vacuum Optical Test (2026.8 – )

## Slide 6
Items | Parameters
Energy band (keV) | 0.4 – 4 keV
Telescope type: | Lobster Eye Optics
Number of Modules | 16
Field of View | 0.53 str (16 modules)
Focal length | 300 mm
Focal plane detectors | pnCCD array
Time resolution | < 100 msec
Sensitivity | ~ 1e-10 (erg/cm2/s) For 100 sec
Position accuracy | 3 arcmin
Micro Pore (Lobster Eye) Optics
Bread Board Model
LEO
CMOS
X-ray collimator
Alignment Adjustment
Before
After
~ 1 arcmin accuracy
Micro Actuators
EAGLE (Wide Field X-ray Monitor)

## Slide 7
ADC
Readout FPGA
PHI Driver
Power Supply
pnCCD
Items | Parameters
Energy band (keV) | 0.4 – 4 keV
Telescope type: | Lobster Eye Optics
Number of Modules | 16
Field of View | 0.53 str (16 modules)
Focal length | 300 mm
Focal plane detectors | pnCCD array
Time resolution | < 100 msec
Sensitivity | ~ 1e-10 (erg/cm2/s) For 100 sec
Position accuracy | 3 arcmin
EAGLE (Wide Field X-ray Monitor)
pnCCD (Focal Imaging Detector)
@+3 degC、150 ms exposure
We have obtained pnCCD driving technology using in-house electronics.
X-ray imaging movie
X-ray spectrum of Mn-Kα/β
Small pnCCD and Readout LSIs
In-house Electronics

## Slide 8
Items | Parameters
Energy band (keV) | 0.4 – 4 keV
Telescope type: | Lobster Eye Optics
Number of Modules | 16
Field of View | 0.53 str (16 modules)
Focal length | 300 mm
Focal plane detectors | pnCCD array
Time resolution | < 100 msec
Sensitivity | ~ 1e-10 (erg/cm2/s) For 100 sec
Position accuracy | 3 arcmin
We evaluated requirements are satisfied
・ Lower detection limit (LD) < 0.3 keV
・ Energy resolution ~ 150 eV @ 5.9 keV
Large-format pnCCD (Focal Imaging Detector)
@ PNSensor (Germany)
@ -60 degC, 10 Hz
Gain Correction
CTI Correction
We started the development of large-format pnCCDs.
EAGLE (Wide Field X-ray Monitor)

## Slide 9
Simulation Studies for Trigger Algorithms
Localization Accuracy
- 80 photons, 1,000 simulations
・ Masking the known bright X-ray sources ・ Search for NEW X-ray sources using a fixed-size window that is shifted across the X-ray image.

## Slide 10
Nominal Operation
(1) A solar separation angle of 120 degrees and Tilted by 50 degrees toward the forward direction.
(2) Keeping the inertial pointing during 560 sec HiZ-GUNDAM monitors X-ray transients
(3) The satellite slews to the next nominal pointing
Maneuver
150 sec
Pointing
560 sec
⦿
Solar
Satellite orbit:
Sun-synchronous polar dawn-dusk orbit
We observe roughly eight different fields of view in every orbit.
This sequence is optimized for follow-up observations with the NIR telescope, we make sure of more than 10 minutes for 97% GRBs discovered by itself.
KSAT
KSAT
Inmarsat
geostationary orbit
Alert message
Coverage : > 90 %
Latency : ~ 0 sec
max delay : 5 min
Inmarsat
Ground Station
HiZ-GUNDAM
Project Server
GCN, Atel

## Slide 11
Fiscal Year | Plans and Milestones
Current | Development of BBM (front loading)
FY2027 | Down Selection Review for 3 candidates (HiZ-GUNDAM / LAPYUTA / Silvia) Establishment of Pre-Project Team
FY2028 | Mission Definition Review
FY2029 | System Definition Review Establishment of Project Team
FY2029 – 30 | EM phase, System Definition Review
FY2030 – 32 | FM phase
FY2034 | Launch
Future Schedule

## Slide 12
High-z Gamma-ray bursts for Unraveling the Dark Ages Mission
Mission Aim: Strong Promotion of
“Time Domain” & “Multi-Messenger Astronomy”.
Items | Parameters
Energy band (keV) | 0.4 – 4 keV
Field of View | 0.53 str (16 modules)
Sensitivity | ~1 e-10 (erg/cm2/s) For 100 sec exposure
Position accuracy | 3 arcmin
Time resolution | < 100 msec
Wide Field X-ray Monitor
Near Infrared Telescope
Observation Strategy
(1) Discovery of high-energy transient with EAGLE
(2) Automatic/Comprehensive follow-up with MONSTER
(3) Sending Quasi-Realtime Alert Messages
(4) Spectroscopy with Large Area Telescopes for selected events
・ Detection of high-redshift GRBs (6 < z < 13 … 20)
・ Probing the reionization history and first metal elements
Key Science2: Probing the Early Universe
Key Science1: Progress of Multi messenger Astronomy
・ Localization of X-ray transients from MM sources
・ Energy transition from gravity to particles/elements
Items | Parameters |  |  |  | 
Aperture size | 30 cm |  |  |  | 
Field of view | 15 arcmin × 15 arcmin |  |  |  | 
Integration time | 10 minutes (2 minutes x 5 frames) |  |  |  | 
Observation Band (μm) | 0.5−0.9 | 0.9−1.3 | 1.3−1.7 | 1.7−2.1 | 2.1-2.5
Limiting mag (AB) | 21.3 | 20.9 | 20.6 | 20.5 | 20.4
・ Lobster Eye Optics
・ pnCCD imaging detector
・ Simultaneous 5-band photometry
・ 0.5 – 2.5 um
MONSTER: Multiband Optical and Near-infrared Simultaneous Telescope for Efficient Response
EAGLE: Exploration of Ancient GRBs with Lobster Eye

## Slide 13
Backup Slides

## Slide 14
Neutral Fraction of H
GRB+
Quasar
Galaxy
(JWST)
Early Epoch Reionization
Late Epoch Reionization
？
Brightest galaxy GN-z11, z=10.60
6 hours exposure (JWST)
Quasar z=7.5 (8 hours exposure)
Bunker+23
Banados+17
High-redshift GRBs are
- Enough bright - Simple spectrum redshift, xHI, galactic neutral gas, metallicity, ionization bubble size, etc.
Cosmic Reionization
Simulation (Umeda & Harikane)
2 hours exposure (Subaru)
z = 10

## Slide 15
12% of all sky
2% of all sky
検出感度 (erg/cm2/s)
観測時間スケール (秒)
Time Scale of X-ray Transient (sec)
Swift/BAT
HiZ-GUNDAM
Time Since Transient Discovery (sec)
Limiting Magnitude (AB magnitude)
Sensitivity of NIR Telescope
Too late
Observation start
Detection Sensitivity
Discovery
Space
GW170817 @ 200 Mpc
15