## Slide 1: Improvement of Expected Performance of MONSTER onboard HiZ-GUNDAM satellite
The third annual conference of Transformative Research Areas (A), “Multimessenger Astrophysics” 18-20 Nov. 2025
ABSTRACT
Current development status of MONSTER, a visible & near-IR telescope onboard HiZ-GUNDAM
Possible improvement of expected scientific performance of MONSTER, namely the detector system
Kohji Tsumura, Rinon Kageyama (Tokyo City Univ.), Hideo Matsuhara, Akihiro Doi, Keisuke Shinozaki (ISAS, JAXA), Shuji Matsuura (Kwansei Gakuin Univ.), Koji Kawabata, Hori Tomoya (Hiroshima Univ.), Hiroshi Akitaya (Chiba Institute of Technology), Daisuke Yonetoku (Kanazawa Univ.) HiZ-GUNDAM / MONSTER team

## Slide 2: List of my talk
1. Introduction - purpose of MONSTER onboard the GRB search satellite
2. Current Design Specifications of MONSTER
3. Key technical challenges in MONSTER development
4. Status of on-going works
  (1) BBM development of MONSTER Telescope
  (2) Imaging sensors
5. Possible improvement of scientific performances
Summary
Notes: Here’s list of my talk, first I introduce the purpose of MONSTER …

## Slide 3
HiZ-GUNDAM satellite
Wide field X-ray Monitor
EAGLE Exploration of Ancient GRBs with Lobster Eye
Visible and near-IR telescope
MONSTER Multiband Optical and Near-IR
Simultaneous Telescope for Efficient Response
Satellite Bus (Attitude control. Data Handling, telecom. etc.)
Notes: On the satellite we have two instruments as show in this figure

## Slide 4: 1. Introduction Quick follow-up is a Key to catch high-z GRB
The afterglow is expected to be brighter than 21mag at 1 hour after the burst (in >90% probability)
19
20
21
22
23
24
25
26
Greiner et al. (2009)
400
600
800
1000
2000
Wavelength (nm)
Magnitude
Optical
NIR
Lyα absorption edge
(121.6 nm @ z=8.3)
Photometry of high-z GRB
1 hour
Gray: Long GRB
Black: Short GRB
Expected Light curve for GRBs @ z = 7
Based on Kann et al. (2010)
1 day
Notes: After an initial flash of gamma rays, a longer-lived "afterglow" is usually emitted.
The brightness of this afterglow become darker with time, so quick follow-up observation is important.
However, the ground based telescopes start to observe them after receiving the alert of GRB from satellites.
So there would be too much delay between GRB event and starting the after-glow observation.
In addition, to observe GRB afterglow at high-redshift GRBs, near-infrared observation is important because optical light are absorbed by the neutral hydrogen.

## Slide 5: 1. Introduction Purpose of MONSTER onboard the GRB search satellite
Ch.1
0.5
1.7
2.1
0.9
1.3
Ch.2
Ch.3
Ch.4
z = 6.4
z = 9.7
z = 13.0
Lyman-alpha
 [µm]
z = 16.3
Ch.5
2.5
z = 19.6
MONSTER wavebands
Rapid (goal: within 15 min) automatic follow-up toward target detected by EAGLE
Identify GRB afterglow & estimate its (crude) photometric redshift
  Redshift can be determined with good accuracy up to z < 13.0.
  In principle, detection is possible up to z < 19.6
J
H
K
Ground telescope
wavebands
Notes: So the reason why MONSTER visible & NIR telescope is onboard the HiZ-gundam, is, to enable rapid automatic follow-up…

## Slide 6: 2. Current Design Specifications of MONSTER
A reflective (offset Gregorian) telescope with 30 cm aperture
Simultaneous 5-band (visible + 4 NIR) imaging via dichroic mirror and a Kösters prism
Field of View: 15 x 15 arcmin2 (12 x 12 un-vignetted) : sufficiently larger than EAGLE error circle (3 arcmin radius) two image sensors(visible and NIR) with 3 arcsec image quality
Cooled Telescope : shall be below 200 K, while the NIR sensor is below 120 K by only passive, radiative cooling system
Telescope structure: all aluminum, athermal design (similarly contraction by cooling)
可視光検出器
近赤外線検出器
Notes: To achieve the purpose, the MONSTER will have the key specifications as below:

## Slide 7: 3. Key technical challenges in MONSTER development
Thermal design, with only passive cooling to cool and maintain telescope below 200 K, detectors below 120 K
  industrial and inhouse study (see R. Kageyama’s poster #62 for in-house study)
Optical: god image quality shall be maintained at cold
  Verification by BBM with “athermal design”
Kösters prism development (see Hori’s talk next)
  a noble beam-splitter splitting incident light into multiple wavelengths on a single image sensor
Image sensors (detectors) with electronics
Onboard image data processing (see H. Niinuma’s poster #57)
With the financial support of Transformative Research Areas (A), we expect to perform all of the above activities. Hereafter I’ll introduce on:
  BBM telescope development and test
  Image Sensor development (commercial CMOS sensor for visible band)

## Slide 8: 4. Status of on-going works (1) BBM development of MONSTER Telescope
Purpose
  Verify the cryogenic optical performance is within the requirement
    demonstration of athermal design (all major structure components are made of Aluminum)
Method
  Modify the existing cryo-vacuum chamber at Kanazawa University
  Image quality at cold is to be measured by introducing a ~30 cmφ collimated beam
Planned Schedule
  FY24: mechanical and thermal design of test configuration
  FY25: design and fabrication of BBM mirrors and structures
  FY26: BBM test in the cryo-vacuum chamber at Kanazawa University
Notes: Here I introduce the status of BBM telescope development

## Slide 9: 4. Status of on-going works (2) Imaging sensors
[ Near-IR detector ]
Teledyne H1RG + SIDCAR (or ACADIA) ASIC
Dark current must be <0.3 e-/s from sensitivity requirement
 temperature < 120 K
requirement
[ Visible-band detector ]
Teledyne HyViSI or Canon LI3030SAM
HyViSI is current baseline, but we also seek for the possibility to use commercially available C-MOS detectors
  Canon LI3030SAM : Cryogenic and radiation tests completed, now onboard control/readout electronics is under study
Canon LI3030SAM
TeledyneH1RG
Notes: Next I will show the status of imaging sensor development.
…
We are planning to use Teledyne H1RG for HiZ-GUNDAM mission.
To obtain a good sensitivity, dark current needs to be low, and it depends on the temperature of the detector.
In our calculation, the detector need to be lower than 150K for channel 2 , and lower than 120 K for channel 3 and 4.

## Slide 10: 4. Status of on-going works (2) Imaging sensors : thermal/electrical architecture
Challenges on commercial CMOS sensor onboard
  Commercially used sensor normally provides us with fast (10~50 fps) readout but with large heat dissipation
  but we only need relatively slow (0.1 – a few fps) readout but low heat dissipation  challenge in the readout/thermal design
  In-house study (with help by two young JAXA members by a scheme of “intra-JAXA internship” )
CMOS sensor
Sensor board
A/D board
Thermal isolation support
Telescope body
~160K
Thermal isolation support
Analog signal Flat cable
Koster Prism module
~160 K
Visible detector ~270K
H1RG
SIDECAR ASIC
NIR detector<120 K
Warm
Control/readout electronics
~300 K
Visible detector electronics
NIR detector electronics

## Slide 11: 5. Possible improvement of scientific performances
Through our current activities we hope to obtain:
By BBM telescope development
  After verifying athermal design, we will also get how the image quality changes with temperature gradient
  → how much can we accept the earthshine illumination to telescope
  → improvement of GRB follow-up capability
By Visible band detector development
  Challenges: slow readout/low heat dissipation, thermal isolation
  Once successful, this is the first visible sensor readout system onboard JAXA astronomical satellite!
  ⇒Prospects to apply for future astronomy mission by JAXA
  Obtain larger FoV for the visible channel:
    LI3030SAM has 4-5 times larger format (with same pix size) than the HiViSI
Notes: Through these activities, we are hoping to improve the scientific performances of MONSTER.
First, verify the athermal design of telescope …
Second, visible sensor readout can be onboard the JAXA astronomical satellite for the first time

## Slide 12: HyViSI vs Commercially available visible sensors
 | Teledyne HyViSI+SideCAR | Sony IMX533CLK | Gpixel GSENSE6060BSI | Cannon LI3030SAM
Pixel number (a) | 1024 × 1024 | 3015 × 3080 | 6144 × 6144 | 2160 × 1286
Pixel size [µm] (b) | 18 | 3.76 | 10.0 | 19
Size [mm] (a × b) | 18.4 ×18.4 |  | 61.4 × 61.4 | 41.04 × 24.32
A/D conversion | 16 bit | 14 bit | 14 bit | 14 bit
Efficiency |  |  | 95% @ 580 nm | 86% @ 550 nm
Readout Noise [e-] | 17 |  | 2.3 (HDR mode) | 3.4 (rms, 40℃)
Dark current [e-/sec] | 0.3 |  | 0.019 @ -55℃ | 300 @ 60℃
Output | Digital | Digital |  | Analog
Comment | Space Flight proven (e.g., JWST) | VERTEX (6U CubeSAT) | Operation guaranteed down to -55℃(218 K) | Space flight (nano-satellite) Tomo-e Gozen (@Kiso Obs.)
Baseline
Option

## Slide 13
Summary
MONSTER onboard HiZ-GUNDAM will provide us with a rapid follow-up capability of targets detected by EAGLE
Possible improvement of science performances
  BBM telescope ⇒ improvement of GRB follow-up capability
  Visible detector ⇒ larger FoV for ch.1; application to future astronomy mission by JAXA
Upcoming Plan (by FY2026)
  Establish the thermal / mechanical design (in-house & industrial studies)
  BBM optical performance test results will be available
  Demonstration of CMOS visible sensor in space-use operation
(1) LARGE FoV (15 x 15 arcmin2)
(2) simultaneous 5-band imaging at 0.5 – 2.5 μm
(3) Passively cooled (radiatively) telescope (< 200 K), and a near-IR detector (<120 K)

## Slide 14: Backup Slides

## Slide 15: Project Status and Planed Master Schedule
Down selection review was held in April-May 2023
  The ISAS Executives recommended that the mission scope be "to produce Key Science results through coordinated observations with space and ground-based telescopes that have been alerted from HiZ-GUNDAM”.
Down selection review (re-examination) in March 2024
  Passed for all the review items
  But the selection is on-hold …
New schedule
  Pre-phase-A study continued
  Continued Mid-2026: Down selection Review with two other candidates
  ~2027: Mission Definition Review
  A new target launch : 2034
Mission concept was selected in 2018 as Competitive M-class Mission
Now in the pre-Phase A study in ISAS/JAXA
Notes: We survived the down-selection eview this year , however
due to serious problems in human resources in both ISAS, JAXA and the industries in charge of spacecraft system

## Slide 16: 可視光・近赤外線望遠鏡BBM試作・実証（2024－6年度）
課題 | 必要な作業 | 実施担当
BBM鏡の製造に向けた検討 | 鏡の製造に必要な検討を実施 | クリスタル光学
BBM鏡の製造 | 実際の鏡の製造、保持機構(裏面構造)含む | クリスタル光学
鏡単体の評価(常温) | 鏡単体の性能評価(干渉計を用いた測定？) | クリスタル光学
望遠鏡システムとしての評価(常温) | ２枚の鏡を組み合わせた望遠鏡システムとしての性能評価(干渉計を用いた測定？) | クリスタル光学
鏡の保持機構の設計 | オプティカルベンチへの鏡の保持機構(望遠鏡裏面でのねじ止めの方法)の検討(表面形状への影響の解析など) | オプトクラフト
望遠鏡のオプティカルベンチの設計 | 金沢チャンバーに入る支持構造の検討 | オプトクラフト・クリスタル光学
金沢チャンバーでの冷却構造の検討 | 金沢チャンバー内へのBBM望遠鏡の設置および冷却の方法についての検討 | オプトクラフト・TAエンジニアリング
金沢チャンバーの整備 | 30cm光学窓の延長など | 
望遠鏡のオプティカルベンチの製造 | 望遠鏡のオプティカルベンチを製造する | 
低温光学実験で用いるコリメーターの選定 | 低温光学試験で用いる口径>30cmのコリメーターの選定 | 
低温光学実験で用いる検出器の選定 | 低温で駆動する必要あり、解像度は必要だが高感度は不要。購入済みのCanon検出期が候補？ | 
金沢チャンバーを用いた低温光学試験の実施 | BBM望遠鏡を冷却(~160K)して光学試験を実施する | 

## Slide 17
ガンマ線バースト (GRB)
・大質量星の爆発 (M>40Msun)
・E = 1050 – 1054 ergs
・非常に明るいため、遠方宇宙の探査に活用できる
Short GRBs (T < 2 sec): 極限環境物理の探査
・中性子星連星の合体
・E = 1048 – 1051 ergs
・重力波との協調観測
Long GRBs (T > 2 sec): 初期宇宙の探査
中性子星連星
など
Notes: Gamma-ray bursts are extremely energetic exposions and they are the brightest and most energetic electromagnetic events known to occur in the universe
There a re two type of GRBs. One is the long GRBs, which are the Massive star explosions, therefoe we can explorer the eary universe at high-z by observing the long GRBs
The other tyoe of GRBs is the short GRB, which caused by the NS-NS merger eith gravitational wave. Therefore, observing short-GRB is very important for the gravitational wave astronomuy

## Slide 18
Nominal Operation
(1) 120 degrees of solar separation angle and 50 degrees of moving forward
(2) Keeping the inertial pointing during 560 sec HiZ-GUNDAM monitors X-ray transients
(3) The satellite slews to the next nominal pointing
Maneuver
150 sec
Pointing
560 sec
⦿
Solar
Satellite orbit:
Sun-synchronous polar orbit (Twilight)
We observe roughly eight different fields of view in every orbit.
This sequence is optimized for follow-up observations with the NIR telescope, we make sure of more than 10 minutes for 97% GRBs discovered by itself.
KSAT
KSAT
VHF
VHF
Inmarsat
down
uplink

## Slide 20
Time Domain Astronomy & Multi Messenger Astronomy
20
z=1000
z=7
z=12
z=0
z=0.5
z=6
・Gravitational Wave
(Short GRB?)
NS-NS, NS-BH (+ BH-BH)
kilonova
・TeV/PeV neutrino
・SN Shock Breakout
・Tidal Disruption
・Fast Radio Burst
・AGN etc.
・Stellar Flare
・Galactic Transients
・Gamma-Ray Burst (GRB)
First Stars (Pop-III)
Cosmic Reionization
Chemical Evolution
Notes: HiZ-GUNDAM is a space mission for both Time domain ＆ Multi-messenger astronomy, like GW. I would emphasize here that, this mission has very unique capability for GRB in the early Universe with its unique capability, which I will explain in the following

## Slide 21: Problems in early universe exploration with conventional GRB follow-ups
Satellite detection of GRBs; alerting it to the ground
⬇︎within 1 hour
Small (30cm-1m) telescopes will detect the afterglow
⬇Within a few hours~1 day
Identify the redshift with a medium size (2~4m) telescope
⬇︎after about 1 day
Spectroscopic observation of high-redshift GRBs with a large 8-m class telescope
By the time a large telescope observes, the GRB afterglow has faded.
In the 18 years of observations with SWIFT, there have been only two GRBs with z>6.
Moreover, statistical accuracy of these spectra is low…
This situation does not change even after the launch of Einstein Probe and SVOM.
Notes: Current situation of GRB follow-ups is:

## Slide 22: Our goal with HiZ-GUNDAM
Satellite detection of GRBs; alerting it to the ground
⬇︎within 1 hour
Small (30cm-1m) telescopes will detect the afterglow
⬇Within a few hours~1 day
Identify the redshift with a medium size (2~4m) telescope
⬇︎after about 1 day
Spectroscopic observation of high-redshift GRBs with a large 8-m class telescope
Accelerates the process from GRB discovery to the realization of follow-up observations with large telescopes.
Because redshifts are measured for all GRBs discovered by HiZ-GUNDAM, almost no high redshift GRBs are missed.
Automatic on-board follow-up within 300 sec
Within an half-hour
Make this happen with HiZ-GUNDAM
Competitive M-class HiZ-GUNDAM

## Slide 23
追観測可能な8m級望遠鏡の分光器の比較
 | Wavelength coverage | Resolution R = R/ΔR | Multiplicity | Notes
Subaru/PFS | Optical + J-band simultaneous | 2000 (blue) 3000 (red) 4000 (NIR) | 2394 fibers | 
Subaru/NINJA | Optical to J, H (+K)-band simultaneous | 5000 | Single object | LTAO => 0.5-1.0 mag deeper than X-shooter
Keck/NIRES | Y, J, H, K simultaneous | 2900 | Single object | 
VLT/X-shooter | Optical to J, H, and K-band simultaneous | 5000 | Single object | 
可視光〜近赤外線を1度の観測でカバーできることが重要

## Slide 24
Wide Field X-ray Monitor
・ Lobster Eye optics
・ pnCCD
Near Infrared Telescope
・ 5-band photometry
HiZ-GUNDAM (High-z Gamma-ray bursts for Unraveling the Dark Ages Mission)
Mission： Time Domain Astronomy
“Multi-messenger astronomy” and “Exploration of the early universe”
Observation strategy
(1) Discovery of GRBs/transients with the wide field X-ray monitor
(2) Automatic repointing (T < 300 sec)
(3) Identification of counterpart with the near infrared telescope
(4) Alert message (T ~<0.5 hour)
(5) Spectroscopic observation with large area telescopes (T 1.5 hr)
Space telescope
8m-class
JWST
Subaru
TMT
GMT
E-ELT
Future 30m-class
We will discover treasured targets from a large amount of transient sources, and provide important observation targets to large area telescopes. We will promote
"exploration of the early universe” & ”MM astronomy"
with all the power of astronomy.
HiZ-GUNDAM (High-z Gamma-ray bursts for Unraveling the Dark Ages Mission)

## Slide 25
Neutral Fraction of H
GRB+
Quasar
Galaxy
(JWST)
Early Epoch Reionization
Late Epoch Reionization
？
Brightest galaxy GN-z11, z=10.60
6 hours exposure (JWST)
Quasar z=7.5 8 hours exposure
Bunker+23
Banados+17
Simulation (Umeda & Harikane)
2 hours exposure (Subaru)
High-redshift GRBs are
- Enough bright - Simple spectrum redshift, xHI, galactic neutral gas, metallicity, ionization bubble size, etc.
GRBs are the best probe for the Cosmic Reionization
Umeda & Harikane

## Slide 26
Further Outcome from HiZ-GUNDAM:
Nucleosynthesis of diverse NS mergers
NS – BH
Infrared = heavy element
IR (red) kilonova (heavy)
Opt (blue) kilonova (light)
Mass
2017
(GW170817、GW＋EM)
NS – NS
We expect “Infrared dominated” kilonova
(Enriched heavy elements, Observed from equatorial direction)
Sensitive Infrared follow-up by HiZ-GUNDAM
2019
(GW190425、GW Only)
2019, 2020
(GW Only)
NS
BH
BH
BH
BH
Mass

## Slide 27: Mission Payload
3
 |  |  | Items | Parameters |  |  |  | 
 |  |  | Telescope type | Offset Optics |  |  |  | 
Items | Parameters |  | Aperture size | 30 cm |  |  |  | 
Energy band (keV) | 0.4 – 4 keV |  | Focal length | 183.5 cm |  |  |  | 
Telescope type: | Lobster Eye Optics |  | F number | F6.1 |  |  |  | 
Module Aperture Size | 192 x 192 mm2 |  | Field of view | 12 arcmin × 12 arcmin |  |  |  | 
Number of Module | 16 |  | FoV per pixel | 2 acsec × 2 arcsec |  |  |  | 
Field of View | 0.5 str (in total) |  | Image size | 3 pixel × 3 pixel |  |  |  | 
Focal length | 300 mm |  | Integration time | 10 minutes (2 minutes x 5 frames) |  |  |  | 
Focal plane detectors | pnCCD array |  | Observation Band (μm) | 0.5−0.9 | 0.9−1.3 | 1.3−1.7 | 1.7−2.1 | 2.1-2.5
Number of pnCCD | 16 |  |  |  |  |  |  | 
Sensitivity | ~1e-10 (erg/cm2/s) for 100 sec |  | Limiting Magnitude mag (AB) | 21.4 | 21.3 | 21.4 | 20.8 | 20.7
Position accuracy | 3 arcmin |  | Focal detector | HyViSi | HgCdTe (H1RG) |  |  | 
Near Infrared Telescope
Focal Plane Image
pnCCD
Lobster Eye Optics
φ300 mm primary
5-band simultaneous photometry
Wide Field X-ray Monitor
Notes: Here I will show the mission instruments, one is Wide Field X-ray monitor, and the another is a near-IR telescope.
The X ray monitor consists of 16 modules of Lobster-Eye Optics and pnCCD focal plane detectors, monitoring 0.5 str simultaneously.
The NIR telescope is a small, 30 cm diameter offset Gregorian telescope, with two focal plane arrays covering 5 photometric bands. Although small diameter telescope, thanks to very low backgropund, the sensitivity is as good as the 2-3 m class telescope in the ground.

## Slide 28: Einstein Probeとの比較
中国(+ESA, MPA)のEinstein Probeが2024年1月に打ち上げ成功、観測開始
２つの観測装置
・ Wide-field X-ray Telescope (WXT): LEO搭載で感度はHZGと同等、従来より1桁高感度
・ Follow-up X-ray Telescope（FXT): 追観測はX線で行う
WXTが高感度なため、従来よりも暗いGRBが多く発見され、この分野でのサイエンスは進むだろう
 HZGチームとしてもEP発見天体に対する追観測計画を検討中
HZGの主サイエンスは遠方GRBの発見  赤外線での即時追観測が肝
EPの追観測スキームは現状と同じ(可視・赤外の即時追観測なし)  イノベーションは起こらない
地上追観測は[昼夜・天域・天気]の制約により観測可能なのは <10% (GRONDの地上追観測の成功率は~4%)
HZGと同感度の3-4m級の地上望遠鏡を全世界に>10台配置するのは困難  衛星自身が即時追観測する事こそがHZGの本質
Einstein Probe

## Slide 29: SVOMとの比較
中国・フランス(+α)のSVOMが2024年6月に打ち上げ成功、観測開始
4つの観測装置
・ ECLAIRs telescope: coded-maskによるGRBの探査 (感度は従来と同程度)
・ Gamma ray monitor (GRM): ガンマ線検出によるGRBの探査
・ Microchannel X-ray Telescope (MXT)：X線での追観測
・ Visible Telescope (VT)：可視光での追観測
GRBの探査は集光光学系(LEO)を持たないので、感度は従来と同程度 (Einstein Probe, HiZ-GUNDAMより感度は1桁悪い)
即時追観測は可視光およびX線のみ (遠方天体を選別できない)
 HZGの本質である近赤外線での即時追観測はHiZ-GUNDAMまで実現される予定はない
SVOM

## Slide 30
[技術要素1] 非励振型高速姿勢変更制御技術（Agility, 機動性）… NEC社の既存技術
[技術要素2] 高精度指向安定化技術（ポインティング安定性） … 新規要素
peak-to-peakで3.2秒角/(120秒) となり、
要求 6秒角/(120秒) を満たすことを確認
高周波微振動外乱、熱環境変化による構造歪み、姿勢による劣化など、
他の要因が指向安定性に及ぼす影響やそれらの配分を評価することが課題
標準小型バスで実現できない機能：高アジリティ、指向精度と安定性の要求値と、その実現性
(1) 高アジリティ要求：
現在の姿勢から +/- 30度の範囲に対して 300 秒で姿勢を変更し、静定すること
(2) 指向精度要求：
絶対指向精度 2 分角（X線で発見した天体を近赤外線望遠鏡の視野に捉える）
(3) 安定性要求：
並進 6秒角/(120秒) p-p… 露光時間120秒における並進誤差が焦点面検出器の 1 ピクセル以内
回転 6.7分角/(600秒) p-p… 追観測 600 秒における回転誤差が焦点面検出器の端で１ピクセル以内

## Slide 31
金属鏡の可視光帯での鏡面精度要求
望遠鏡・主構造ともオールアルミのアサーマル設計を想定
- 球面鏡の試作を行い表面粗さとして peak-to-valley で約 11nm を実現
- 加工者の経験から非球面鏡であっても同精度を達成することができることを確認
最短波長 500 nm に対して 1/40 以下となり、鏡面精度要求は十分に満たしている
倍率：1.3倍
Sa :10.964 nm
倍率：10倍
Sa ：8.669 nm
「締結時の鏡面湾曲の低減」と「取り付けの再現性」 をさらに検討する。
FY2025 に主構造を含む実機モデル（BBM）を製造して自由曲面鏡の鏡面精度を
評価するとともに、低温環境化での結像性能について評価する予定。

## Slide 32
フェーズ | スタッフ | 大学院生 | 企業
2012年〜2018年 （WG 設立から提案まで） | 14 FTE (2人 x 7年) | 35 FTE (5 人 x 7年) | -
2019年〜2025年 （提案から現在まで） | 30 FTE (5 人 x 6年) | 48 FTE (8 人 x 6年) | -
今後の検討期間 | 32 FTE (8 人 x 4 年) | 40 FTE (10 人 x 4 年) | -
プロジェクト建設期 | 75 FTE (15 人 x 5 年) | 100 FTE (20 人 x 5 年) | 200 FTE (40 人 x 5 年)
観測期 | 15 FTE (5 人 x 3 年) | 30 FTE (10 人 x 3 年) | -
※ 人数はエフォート率を掛けた後の人数
プロジェクト実現に必要な総FTE(人年)の見積り 総FTEには開発・サイエンス検討・運用の全てを含む
プロジェクト建設期で想定する FTE 数
JAXAメンバーの数：7 FTE/年
大学等のメンバーの数：スタッフ 8 FTE/年、大学院生 20 FTE/年
光赤外線分野：
JAXAメンバーの数：1.5 FTE
大学等のメンバーの数：3 FTE
合計 約600 FTE

## Slide 33
宇宙研での審査状況
2024年3月にダウンセレクション（再審査）
- ミッションの意義・価値・要求設定、システム実現性、ミッション定義フェーズの活動 に対しては妥当との評価。
- プロジェクト計画に対しては概ね妥当と評価 JAXA のプロジェクトマネージャ、システムマネージャ等を定めていく必要がある
しかしながら、 - 衛星システムメーカの人員不足
- JAXA のプロジェクトマネージメント体制の人員不足により、宇宙研執行部の「経営判断」として選定は「保留」という状況
2026年頃に、HiZ-GUNDAM / SILVIA / LAPYUTA の 3 候補で改めてダウンセレクション 選定されたミッションはプロジェクト化へ向けた活動を行い、残りの２つはワーキンググループへ立ち戻ることになる。
2024/05/08
宇宙理工学合同委員会にて決定
想定するスケジュール